## Slide 1: AWS-UCF PINN Research
UCF Team
Andre Von Zuben
Augusto Marques
Felipe Viana
AWS Team
Ankur Srivastava
Srinivas Tadepalli
Ana Simoes
Sundar Ranganathan
Ryan Qi
Adam Rasheed
Michael Curry

## Slide 2: Logistics
UCF-AWS-PINN-SHARE on OneDrive
Shared with: aqsimoes@amazon.com; tadeps@amazon.com; mahaaws@amazon.com; rangasun@amazon.com; awsrashe@amazon.com; awsankur@amazon.com; ryanqi@amazon.com.
Anybody else?
GitHub repository
Could you send me your GitHub user information?

## Slide 3: Proposed workflow
6) Run solver
1) Generate geometry
2. Annotate equilibrium, BC, and material and generate baseline mesh
3) Generate file with collocation points
4) Customize (template) Python code for equilibrium, BC, and material
5) Generate solver setup files
Major hypothesis tested:
From geometry to collocation points: use engineering software (FreeCAD) and get baseline mesh, which defines problem through annotation. Densification can be applied if needed.
Split domain with specialized loss functions (equilibrium, initial condition, boundary conditions).
DDP implementation and deployment
Parametric modeling
Third party
Potential interface with other packages
Bulk of parallelization
from mesh
densified
Finished
Almost finished
Current work

## Slide 4: Navier-Stokes in the velocity-pressure (VP) form
(a) Approach to improve solution from Modulus (SimNet)
Most papers use the velocity-pressure (VP) form
in
in
such that (Dirichlet and Neumann)
in
in
Observations
In these papers, besides the PDEs, actual observations are used to estimate and .
Many report problems regarding training convergence.

## Slide 5: Navier-Stokes in the stress tensor (ST) form
(a) Balance of mass in VP form
in
Achieved in 2D by using the stream function , such that
and
which makes ()
Practitioners have added further constraints to improve convergence (see Modulus documentation); or alternatively, used other formulations.
(b) ST form and balance of mass
in
in
in
such that (Dirichlet and Neumann)
in
in
Observations:
Balance of mass:
DNN training: the ST form reduces the order of derivatives compared to the VP form.

## Slide 6: Laminar and steady state (explicitly making
(b) VP formulation*
*Using our PyTorch implementation
**Using a TF1 implementation from Rao et al. (2020) (our implementation works the same)
(c) ST formulation**
Loss = 5.54
Iterations = 24,000
Wall clock time = 19h
Loss =
Iterations = 37,234
Wall clock time = 30h
(a) OpenFOAM

## Slide 7: Transient and flow with mild Kalman vortexes
*Using our PyTorch implementation
**Using a TF1 implementation from Rao et al. (2020) (our implementation works the same)
Loss = 841
Iterations = 2300
Loss =264
Iterations = 35000
(b) VP formulation*
(c) ST formulation**
(a) OpenFOAM

## Slide 8: Transient and laminar flow
(a) OpenFOAM
(b) ST formulation
GIF
Incorporated ST formulation in our PyTorch implementation
PINN captures time-dependent response with realistic prediction
Optimization needs to be improved

## Slide 9: Improving PINN optimization
Literature has recognized need for specialized training schemes
(a) Increase
CFD: warm start
(b) Adaptive learning rate
CFD: --
Regular training
Warm start
Iterations
https://proceedings.neurips.cc/paper/2021/file/df438e5206f31600e6ae4af72f2725f1-Paper.pdf
(c) Euler initialization (we are proposing)
CFD: “hybrid initialization”
Frictionless flow:
As opposed to
: learning rate
and are dynamically adjusted throughout training
https://www.sciencedirect.com/science/article/pii/S0021999120307257
(d) Vary collocation point density
CFD: multigrid
Versteeg, H. K., Malalasekera, W. (2007). An Introduction to Computational Fluid Dynamics: The Finite Volume Method.
Level 1
Level 5

## Slide 10: If mass balance continues to be a problem
Conservation principle:
Mass flow going into the element is equal to mass flow going out of the element
At the element level:
Integrate the domain and add a mass flow conservation component to the loss:
Observations:
Eliminate heuristic regarding “conservation planes”
Replace element nodes with edge/face centroid
2D and 3D formulations are the same
, velocity
, normal to the element edge/face
, length/area of the element edge/face
Legend
Element
Node (collocation point)

## Slide 13: Needed improvement: training schemes
Literature has recognized need for specialized training schemes
(b) Increase
CFD: warm start
(a) Vary collocation point density
CFD: multigrid
(c) Adaptive learning rate
CFD: --
Versteeg, H. K., Malalasekera, W. (2007). An Introduction to Computational Fluid Dynamics: The Finite Volume Method.
Regular training
Warm start
Iterations
https://proceedings.neurips.cc/paper/2021/file/df438e5206f31600e6ae4af72f2725f1-Paper.pdf
(d) Euler initialization (we propose)
CFD: hybrid initialization
Level 1
Level 5
: learning rate
and are dynamically adjusted throughout training
https://www.sciencedirect.com/science/article/pii/S0021999120307257
Starts with a frictionless flow

## Slide 14: Schedule
Month within the period of performance | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb
Pre-processing routines |  |  |  |  |  |  |  |  |  |  |  | 
Read geometry files |  |  |  |  |  |  |  |  |  |  |  | 
Generate collocation points (mesh) |  |  |  |  |  |  |  |  |  |  |  | 
Processing routines |  |  |  |  |  |  |  |  |  |  |  | 
Implement PINN solver |  |  |  |  |  |  |  |  |  |  |  | 
Establish default parameters |  |  |  |  |  |  |  |  |  |  |  | 
Post-processing routines (visualization) |  |  |  |  |  |  |  |  |  |  |  | 
Generate standard files (for FE software) |  |  |  |  |  |  |  |  |  |  |  | 
Generate rendering routines |  |  |  |  |  |  |  |  |  |  |  | 
Verification and validation |  |  |  |  |  |  |  |  |  |  |  | 
Use agreed upon case studies |  |  |  |  |  |  |  |  |  |  |  | 
Skeleton of many routines (pre-processing and processing) in place
We will get into packaging them in classes and improve solver robustness (neural network initialization, handling collocation point and losses, optimizer, etc.)

## Slide 15: Neural net initialization idea (beg, borrow, steal)
https://apps.dtic.mil/sti/pdfs/AD1069198.pdf
https://proceedings.neurips.cc/paper/2021/file/df438e5206f31600e6ae4af72f2725f1-Paper.pdf

## Slide 16: Tracking gradients
http://proceedings.mlr.press/v9/glorot10a/glorot10a.pdf
https://epubs.siam.org/doi/pdf/10.1137/20M1318043

## Slide 17: Architecture
https://epubs.siam.org/doi/pdf/10.1137/20M1318043

## Slide 18: Dealing with time (beg, borrow, steal?)
https://proceedings.neurips.cc/paper/2021/file/df438e5206f31600e6ae4af72f2725f1-Paper.pdf

## Slide 19: Study cases
Case​ |  | Ground truth​ | PINN (Vanilla and others)​ | ​
1D​ | ​ | Exact solution​ | ​ | ​
 | ​ | Exact solution​ | C-PINN​ | ​
2D​ | ​ | OpenFoam​ | ​ | ​
3D​ | ​ | FreeCad​ | Modulus​ | ​
 | ​ | OpenFoam​ | Modulus​ | ​
Burgers' equation
Convection equation
Flow around a cylinder
Deflection of a bracket
Flow in aneurysm

## Slide 20: Draft and old

## Slide 21: Estimating data size
ImageNet = 150GB
English Wikipedia = 20.69 GB
c4/en = 866.42 GB
c4/multilingual = 29.42 TB
Baseline cases (float32)
 | Steady-state |  | Transient | 
Collocation points | 1M |  | 1M | 
Time steps | 1 |  | 1,000 | 
DOE size | 1 | 50 | 1 | 50
Data size | 12 MB | 600 MB | 12 GB | 600 GB

## Slide 22: Distributed training (recap)
Blindly breaking collocation points into processes (GPUs) might work for small problems, but it does not scale well with data
A major problem is the mix of collocation points coming from equilibrium, boundary conditions, and initial conditions.
DOE points

## Slide 23: New stochastic dynamic batching
1) Create DOE points:
Fraction of or all IC from DOE#1
h5 #1
Fraction of or all BC from DOE#1
h5 #2
Fraction of equilibrium from DOE#1
h5 #4
Fraction of or all BC from DOE#1
h5 #3
Fraction of equilibrium from DOE#N
h5 #
...
2) Create h5 files:
3) Iterate over h5 files
Validation
h5 #1
h5 #2
h5 #
...
h5 #
h5 #
...
Compute gradients for weights and biases
Update model parameters
Compute loss at all h5 files
Training
h5 #1
h5 #2
h5 #4
h5 #3
h5 #
...
File
Probability
4) Choose h5 files for next iterations
Probabilities are computed from (reduced) loss functions on a file-by-file basis
Probabilities are proportional to loss (higher losses are likely to be used as training again)
5) Go back to step 3 and repeat until convergence
Each h5 file has only one head (computation efficiency)
This scheme is computationally efficient:
h5 files have only one head, therefore only one dynamic graph executed within each the GPU
Probabilities are computed with losses as they are reduced and sent back to host process
No need to force convergence at IC/BC points since larger errors would drive higher losses and therefore higher probabilities in step 4

## Slide 24: To-do list
Augusto:
1) Find architecture from literature that works (preferably in PyTorch)
https://github.com/Raocp/PINN-laminar-flow
2) Cluster collocation points
3) Continuity collocation points with normal vectors
2D: collocation points = half-way between nodes for each element
3D: collocation points = barycenter of faces
Normal vectors saved as annotation within new continuity
3) Aneurism
Andre:
Implement h5 sampling algorithm -> 50 files (100 total) – 20 seconds; evaluation: 500 files (100 samples) – 32 seconds
Cluster collocation points
Andre and Augusto
Connectivity matrix trick for conservation of mass

## Slide 25: Testing Navier Stokes implementation
Run ground truth using OpenFoam
Ideally run original code (might have to create a new Python environment)
Run our PyTorch implementation with setup as similar as possible (don’t break down domain in multiple h5 files yet)
Run implementation with multiple h5 files
Use case 1: Creeping flow
Reproduce
https://github.com/Raocp/PINN-laminar-flow
Use case 2: Flow with vortex shedding
Re = 62.9
Umax = 6.29 m/s
Run ground truth using OpenFoam
Ideally run “Raocp” code (might have to create a new Python environment)
Run our PyTorch implementation with setup as similar as possible (don’t break down domain in multiple h5 files yet)
Run implementation with multiple h5 files
TRY WITHOUT CONSERVATION OF MASS FIRST

## Slide 26: Navier Stokes formulations
https://arc.aiaa.org/doi/abs/10.2514/6.2022-1436 (See OneDrive)

## Slide 28: Old stuff

## Slide 29: Test case: Burgers’ equation
BC
IC
0
1
t
-1
1
x
h5 files
Equilibrium (2 files)
Setup:
4 h5 files
  1 IC (100), 1 BC (200), 2 Eq (5000 ea)
4 processes
(b) Stochastic dynamic batching (4 files / 4 proc)
(a) Baseline - traditional PINN implementation

## Slide 30: Test with #points in Eq. > #points in IC and BC
(a) 2 processes
(a) 6 processes
(a) 10 processes
(a) 20 processes
#points: 100 IC – 200 BC – 10,000 Eq. / 8 h5 files: 2 IC (50 ea), 2 BC (100 ea), 4 Eq (2500 ea)

## Slide 31: Test with #points in Eq. #points in IC and BC
(a) 10 processes
(a) 20 processes
(a) 50 processes
(a) 200 processes
#points: 1,600 IC – 1,600 BC – 6,400 Eq. / 96 h5 files – 16 IC (100 ea), 16 BC (100 ea), 64 Eq (100 ea)
(a) 100 processes

## Slide 32: Navier-Stokes
Spatial points:
  Inlet: 182 (1 h5)
  Outlet: 182 (1 h5)
  noSlip1: 362 (2 h5)
  noSlip2: 240 (1 h5)
  noSlip3: 362 (2 h5)
  NavierStokes: 38,460
Time steps: 2501 (0 to 5 – 0.002 step size)
Total data points: 96,188,460
H5s
  12,943 (1,000/10,000) – 18 min
  999 (100,000) – 15 min
  999 (100,000 – valid 100) – 37 sec
    20 hours/500 iterations of 100 files

## Slide 33: Transient fluid dynamics problem (Navier-Stokes)
30D
20D
D = 0.1 m
10D
Inlet velocity profile
2D Incompressible flow
Laminar flow
1.5 ≤ Re ≤ 150

## Slide 34: Dataset for performance comparison
Re = 1.5
Umax =0.15 m/s
Re = 62.9
Umax =6.29 m/s
Re = 150
Umax =15 m/s
Examples for

## Slide 35: POD Implementation
https://github.com/mathLab/EZyRB
The EZyRB Python package performs a proper orthogonal decomposition with SVD (NumPy) and interpolation with RBFInterpolator (SciPy)
The POD with Interpolation is built upon the numerical data obtained by the original model (in our case, OpenFoam)

## Slide 36: Parametric study of Umax (10 data points)
Testing set
OpenFoam
POD
Umax (m/s)
3.73
9.37
13.98
0.15
15.00
Training set
U
4.05
0.00
0.00
0.00
11.03
17.64
Difference
ΔU (m/s)
RMSE = 3.74 e-3
RMSE = 0.57
RMSE = 0.55
4.3
-5
0.0
Testing points
Training points
Umax = 3.73
Umax = 13.98
Umax = 9.37

## Slide 37: Parametric study of Umax and nu (20 data points)

## Slide 38: Dataset for performance comparison
Re = 1.5
Umax =0.15 m/s
Re = 67.5
Umax =6.75 m/s
Re = 150
Umax =15 m/s
Examples for
Varying param |  |  | Training points | Test points
() | [0.15 , 15] | 0.01 | 10 and 20 | 30
() | 1 | [, ] | 10 and 20 | 30
and | [0.15 , 1.5] | [, ] | 20 and 40 | 60
Varying param |  |  | Training points | Test points
 | [0.15 , 15] | 0.01 | 10 and 20 | 30
 | 1 |  | 10 and 20 | 30
 | [0.15 , 1.5] |  | 20 and 40 | 60

## Slide 39: Results: number of files and processes
Persistence of validation/training loss and dynamic batching
Flag dynamic batching
Scale number of h5 files
  2 IC (50 ea), 2 BC (100 ea), 4 Eq (2500 ea) – 2 / 5 / 10 / 20 processes
  16 IC (100 ea), 16 BC (100 ea), 64 Eq (100 ea) – 10 / 20 / 50 / 100 / 200 processes
  2 IC (100 ea), 2 BC (200 ea), 4 Eq (1000 / 2500 / 5000 ea)
  16 IC, 16 BC, 64 Eq (1000 / 2500 / 5000 ea) – 10 / 20 / 50 / 100 / 200 processes
Loss vs iteration
#files (IC, BC, Eq.) vs iteration

## Slide 40: Results: number of files and processes (cont’d)
Andre (and Renato)

## Slide 41
DataPartitioner
GPU 1
Optimizer
HOST
All-reduce
PINN
Scatter data
GPU 2
Optimizer
PINN
GPU 3
Optimizer
PINN
GPU N
Optimizer
PINN
GPU 1
Optimizer
PINN
GPU 2
Optimizer
PINN
GPU 3
Optimizer
PINN
GPU N
Optimizer
PINN

## Slide 42
DataPartitioner
GPU 1
GPU 2
GPU 3
GPU N
Optimizer
HOST
Broadcast
Gather/
Reduce
PINN
PINN
PINN
PINN
Scatter data
DOE points:
Single-machine (cluster) multi-GPU
Next
Implementation based on the Distributed Data-Parallel Training (DDP) paradigm

## Slide 43: Estimating data size
Baseline case : 1M collocation points, 50 doe points, 1,000 time steps, float32 =600 GB, float64=1,200 GB
ImageNet = 150GB, English Wikipedia = 20.69 GB, c4/en = 866.42 GB, c4/multilingual = 29.42 TB
Baseline case
 | Steady-state |  | Transient | 
Collocation points | 1M |  | 1M | 
DOE size | 1 | 50 | 1 | 50
Time steps | 1 |  | 1,000 | 
Data size |  |  | 12 GB | 60 GB

## Slide 44: Test case: Burgers’ equation
BC
IC
0
1
t
-1
1
x
h5 files
Equilibrium (2 files)
Setup:
4 h5 files
  1 IC (100), 1 BC (200), 2 Eq (5000 ea)
4 processes
(b) Stochastic dynamic batching (4 files / 4 proc)
(a) Baseline - traditional PINN implementation

## Slide 45: Test with #points in Eq. > #points in IC and BC
(a) 2 processes
(a) 6 processes
(a) 10 processes
(a) 20 processes
#points: 100 IC – 200 BC – 10,000 Eq. / 8 h5 files: 2 IC (50 ea), 2 BC (100 ea), 4 Eq (2500 ea)

## Slide 46: Test with #points in Eq. #points in IC and BC
(a) 10 processes
(a) 20 processes
(a) 50 processes
(a) 200 processes
#points: 1,600 IC – 1,600 BC – 6,400 Eq. / 96 h5 files – 16 IC (100 ea), 16 BC (100 ea), 64 Eq (100 ea)
(a) 100 processes

## Slide 47: From physics to classes
Burger’s equation:
subjected to:
where is the viscosity
Physics
Classes
BurgersBC
BurgersIC
0
1
t
-1
1
x
Annotation in vtk file
Burgers
class Burgers(TrainingHead):
def __init__(self, theta) -> None:
super(Burgers, self).__init__()
self.theta = theta
def get_variables(self, inputs):
x = inputs[:, :1].requires_grad_()
t = inputs[:, 1:].requires_grad_()
variables = (x, t)
return torch.cat(variables, 1), variables
def forward(self, u, x, t):
u_x = torch.autograd.grad(u, x, ...)[0]
u_t = torch.autograd.grad(u, t, ...)[0]
u_xx = torch.autograd.grad(u_x, x, ...)[0]
f = u_t + u * u_x - self.theta * u_xx
return f

## Slide 48: From physics to classes
Burger’s equation:
subjected to:
where is the viscosity
Physics
Classes
BurgersBC
BurgersIC
0
1
t
-1
1
x
Annotation in vtk file
Burgers
class BurgersIC(TrainingHead):
def __init__(self, a) -> None:
super(BurgersIC, self).__init__()
self.a = a
def get_variables(self, inputs):
x = inputs[:, :1]
return inputs, (x, )
def forward(self, u, x):
return u - (-self.a * torch.sin(np.pi * x))
class BurgersBC(TrainingHead):
def __init__(self) -> None:
super(BurgersBC, self).__init__()
def get_variables(self, inputs):
return inputs, (inputs, )
def forward(self, u, variables):
return u

## Slide 49: Snippets of code: PINNModel and Training loop
class PINNModel(nn.Module):
def __init__(self, net, training_heads):
self.net = net
self.training_heads = training_heads
def forward(self, x, key):
head = self.training_heads[key]
x, variables = head.get_variables(x)
x = self.net(x)
x = head(x, *variables)
return x
PINNModel
net = Net()
training_heads = nn.ModuleDict({
'Burgers': Burgers(0.01 / np.pi),
'BurgersIC': BurgersIC(1),
'BurgersBC': BurgersBC(),
})
model = PINNModel(net, training_heads)
Model creation
for data, target in train_dataloader:
optimizer.zero_grad()
loss_eq = F.mse_loss(model(data, 'Burgers'), target)
loss_ic = F.mse_loss(model(ic_data, 'BurgersIC'), ic_target)
loss_bc = F.mse_loss(model(bc_data, 'BurgersBC'), bc_target)
loss = loss_eq + loss_ic + loss_bc
accelerator.backward(loss)
optimizer.step()
Training loop
2 Nvidia Tesla P100 16GB
Training heads: 3 min 53 sec
Previous prototype: 3 min 18 sec
Local CPU (10x)
~ 13 min

## Slide 50: Classes for Navier-Stokes 2D (incompressible)
class NavierStokes2D(TrainingHead):
def __init__(self, rho, mu, fx=0, fy=0) -> None:
super(NavierStokes2D, self).__init__()
self.rho = rho
self.fx = fx
self.fy = fy
self.mu = mu
def get_variables(self, inputs):
x = inputs[:, :1].requires_grad_()
y = inputs[:, 1:2].requires_grad_()
t = inputs[:, 2:].requires_grad_()
variables = (x, y, t)
return torch.cat(variables, 1), variables
def forward(self, psi_p, x, y, t):
psi = psi_p[:, :1] p = psi_p[:, 1:] u = torch.autograd.grad(psi, y, ...)[0]
.
.
mx = self.rho * (u_t + u*u_x + v*u_y) + p_x - self.rho*self.fx - self.mu *(u_xx + u_yy)
return u, v, mx, my

## Slide 51: Classes for Navier-Stokes 2D (incompressible)
class VelocityBC(TrainingHead):
def __init__(self, u,v) -> None:
super(VelocityBC, self).__init__()
self.u = u
self.v = v
def get_variables(self, inputs):
x = inputs[:, :1].requires_grad_()
y = inputs[:, 1:2].requires_grad_()
t = inputs[:, 2:]
return torch.cat((x, y, t), 1), (x, y)
def forward(self, psi_p, x, y):
psi = psi_p[:, :1] p = psi_p[:, 1:]
u = torch.autograd.grad(psi, y,...)[0]
v = -torch.autograd.grad(psi, x,...)[0]
return u - self.u, v-self.v
class WallBC(TrainingHead):
def __init__(self) -> None:
super(WallBC, self).__init__()
def get_variables(self, inputs):
x = inputs[:, :1].requires_grad_()
y = inputs[:, 1:2].requires_grad_()
t = inputs[:, 2:]
return torch.cat((x, y, t), 1), (x, y)
def forward(self,psi_p, x, y):
psi = psi_p[:, :1]
p = psi_p[:, 1:]
u = torch.autograd.grad(psi, y,...)[0]
v = -torch.autograd.grad(psi, x,...)[0]
return u - torch.zeros_like(u),
v-torch.zeros_like(v)

## Slide 52: Parametric modeling - Renato
Burger’s equation:
subjected to:
where is the viscosity
Case study:
Training vs validation
Propagation of uncertainty

## Slide 53: Navier Stokes - Augusto

## Slide 54: DataLoader - Andre

## Slide 55: Parametric models

## Slide 56: Training
Training:
10,000 epochs
4 hours (investigating issue, maybe installation)
Boundary conditions
Initial conditions
20 sampled values for density :
10,000 collocation points (from grid):
Prediction: 0.002 secs/instance of
10
0
1
t
-1
1
x

## Slide 57: Validation
Velocity field
Parametric
Stand alone
0
1
t
-1
1
x
-1.75
-1.50
0.75
0
0.25
+1
-1

## Slide 58: Propagation of uncertainty
Y = Net(cat((x,t,nu), dim=1))

## Slide 59: Accelerate – handling different distributed settings

## Slide 60: Why Accelerate
Easy API to make the same code run seamlessly on local machine or different distributed environments.
my_model.to(device)
for batch in my_dataloader:
my_optimizer.zero_grad()
inputs, targets = batch
inputs = inputs.to(device)
targets = targets.to(device)
outputs = my_model(inputs)
loss = my_loss_function(outputs, targets)
loss.backward()
my_optimizer.step()
Original code (plain vanilla)
from accelerate import Accelerator
accelerator = Accelerator()
device = accelerator.device
my_model.to(device)
my_model,my_optimizer,my_dataloader = accelerator.prepare(my_model,my_optimizer,my_dataloader)
for batch in my_dataloader:
my_optimizer.zero_grad()
inputs, targets = batch
inputs = inputs.to(device)
targets = targets.to(device)
outputs = my_model(inputs)
loss = my_loss_function(outputs, targets)
accelerator.backward(loss)
my_optimizer.step()
“Accelerate” version (DDP ready)
CLI tool that allows easy lauching:
$ accelerate launch my_script.py --args_to_my_script
Supported integrations: CPU only / single GPU multi-GPU on one node or several nodes / TPU / FP16 with native AMP

## Slide 61: Snippets of code: Burgers’ equation
def run(epochs=10, verbose=False):
accelerator = Accelerator()
...
train_dataloader = torch.utils.data.DataLoader(train_set, batch_size=bsz, shuffle=True)
train_bc_dataloader = torch.utils.data.DataLoader(train_set_bc, batch_size=bsz_bc,
shuffle=True)
model = Net()
model = model
optimizer = optim.Adam(model.parameters(), lr=0.002)
model, optimizer, train_dataloader, train_bc_dataloader = accelerator.prepare(
model, optimizer, train_dataloader, train_bc_dataloader)
...
for epoch range(epochs) :
...
for data in train_dataloader:
...
accelerator.backward(loss)
optimizer.step()
...
Implementation using Accelerate

## Slide 62: Snippets of code: Burgers’ equation
...
if (epoch+1) % 10 == 0:
avg_loss = epoch_loss / num_batches
accelerator.reduce(avg_loss, 'mean')
accelerator.wait_for_everyone()
if accelerator.is_main_process:
if verbose:
print(f'Avg Loss at epoch {epoch}: {avg_loss}')
if avg_loss < best_loss:
if verbose:
print(f'Avg Loss improved from: {best_loss} to {avg_loss}')
best_loss = avg_loss
unwrapped_model = accelerator.unwrap_model(model)
accelerator.save(unwrapped_model.state_dict(), 'burgers_model.pt')
...
Implementation using Accelerate

## Slide 63: Snippets of code: Burgers’ equation
Accelerate config file for a 2-GPU Linux machine

## Slide 64: Running on a 2-GPU Linux machine

## Slide 65: Implementing distributed training – GPUs (Linux machine)
5000 Epochs, 2 Nvidia Tesla P100 16GB (3 min 18 secs)

## Slide 66: Implementing distributed training – CPU (laptop)
5000 Epochs, 10 process, local CPU (~ 13 min)

## Slide 67: Designing classes

## Slide 68: Training Head
class Burgers(TrainingHead):
def __init__(self) -> None:
super(Burgers, self).__init__()
def forward(self, inputs, u):
x = inputs[:,:1]
t = inputs[:,1:2]
nu = inputs[:,2:]
u_x = torch.autograd.grad(u, x,
create_graph=True,
grad_outputs=torch.ones_like(x),
allow_unused=True)[0]
u_t = torch.autograd.grad(u, t,
create_graph=True,
grad_outputs=torch.ones_like(t),
allow_unused=True)[0]
u_xx = torch.autograd.grad(u_x, x,
create_graph=True,
grad_outputs=torch.ones_like(u_x),
allow_unused=True)[0]
f = u_t + u*u_x - nu*u_xx
return f

## Slide 69: DataLoader
Compatible with PyTorch and Accelerate
- n_partitions : int
- bcs : dict
- variables : list
PINNDataset
+ PINNDataset(collocation_points, variables, …)
+ get_partition(n)
def get_partition(self, n=0, device=None):
points = {}
for bc in self.bcs:
nn = n % self.bcs[bc]['n_partitions']
if nn == self.bcs[bc]['n_partitions'] - 1:
points[bc] = self.bcs[bc]['points'][nn * self.bcs[bc]['partition_size']:]
else:
points[bc] = self.bcs[bc]['points'][nn * self.bcs[bc]['partition_size']:(nn + 1) * self.bcs[bc]['partition_size']]
return PINNDatasetPartition(points, self.variables, device)
- points : dict
- variables : list
- device : torch.device
PINNDatasetPartition
+ PINNDatasetPartition(points, variables, …)
# __len__()
# __getitem__(index)
Within the training loop:
for batch in my_dataloader:
my_optimizer.zero_grad()
inputs, targets, th_key = batch
training_head = training_heads[th_key]
...

## Slide 70: Parametric models

## Slide 71: Parametric modeling (Augusto)
Burger’s equation:
subjected to:
where is the viscosity and is the amplitude of the initial condition
Case study:
Training vs validation
Propagation of uncertainty

## Slide 72: Training
DOE
GIF

## Slide 73: Validation
DOE
Blue – training
Black - validation
Parametric
Stand alone
Difference

## Slide 74: Propagation of uncertainty
Y=Net(cat([x,t,nu,A]))
X= 0.5
0 <= T <= 1
-1 <= X <= 1
T= 0.75
X= 0.5
T= 0.5

## Slide 75: Whiteboard
Things to consider:
Large computational mechanics models (FEA, CFD) can have meshes with millions of nodes.
Candidate classes:
PINNDataset: data set for our PINN (see next slide)
DistributedEnvironment: the objects could be instantiated using config files
DataPartitioner: this is what we have already started implementing.
  For now, we want to be able to control the proportion of equilibrium only versus BC/IC points
  We might want to give to users the freedom to split the data (training, test, validation)
  Later, we should modify the training such that we are actually solving a constrained optimization problem
Architecture: any neural net, for now we have been using vanilla MLPs, but should be open to other architectures. Modulus has a rich collection of architectures.
DifferentialOperators: this should be NN heads added to PINN during training, they should be associated with equilibrium, boundary, and initial conditions.
PartialDifferentialEquations: this could be specialized set of differential operators for certain physics/engineering problems, such as: NavierStokes, LinearElasticity, etc. Modulus does a good job here.
LossScalingFactor: this class could be used to scale/normalize the loss associated with equilibrium, boundary, and initial conditions
Callbacks: we should/could use native PyTorch and that can come from config files (Logger, EarlyStopping, LearnRateScheduler, ReduceLROnPlateau, ModelCheckpoint, etc.). SciANN has a rich collection of Callbacks.
Solver (training): this could be interesting if we decide to wrap the optimization here. It could accommodate variations on the theme (DataPartitioner, Loss, etc.).
Solver (prediction): should also consider prediction loop that can be tied to different use cases, such as design optimization or uncertainty quantification.

## Slide 76: TO DO
Points for discussion:
Implement ﻿burgers_ddp with “from torch.nn.parallel import DistributedDataParallel as DDP?”
Implementations:
  From DOE file (csv or json) to ﻿torch.utils.data.Dataset
    Can/should create a class for this (PINNDataset)
    Each collocation point should have: inputs, targets, heads, losses
      Inputs: need to figure how to stack xyzt with user-defined variables
        Mesh and DOE without duplication during loading
        Duplication happens when passing to workers
      Targets: some DOE points might have results from FEA or CFD (need to figure out how to stuff that in the file system (e.g., /data_trng/data_01.vtk also has the ground truth)
      Differential operators (PINNHead) and losses: together as a neural network head (nn.Module) indexed per collocation point so that “DataSplitter” can return the tuple.
      Head: set of DifferentialOperators or PartialDifferentialEquations all dependent on the annotations in the vtk file (for now, a DOE point either has a target or a set of heads)
      Losses: for now a lot will be MSE, but we should make it flexible. A collocation point might have more than one head when it belongs to BCs/ICs (one loss for the equilibrium and another for the BCs/ICs).
  PINNHead:
    forward(): user implements physics
    loss(): default MSE.
  PINN:
    Differentiate between
      forward(self, inputs): plain vanilla from inputs through field prediction
      forward(self, PINNDataset): from inputs through field prediction and heads
    Or have PINNEquilibrium / PINNDirichlet/etc...
  Burgers with variable amplitude (or frequency)
  Any further study on HuggingFace’s Accelerate?

## Slide 77: TO DO
Andre:
Install PyTorch (cuda env.) on Alan
Run Accelerate version of burgers_ddp.py on Alan
PINNDataset
Renato:
Run Accelerate version of burgers_ddp.py somewhere else (multiple GPUs and TPU-colab)
Augusto:
Run burgers with A and nu as input variables (use burgers_ddp.py)
PINNHead:
  Mother class
  Child classes:
    class Burgers(PINNHead)
    class InitialCondition(PINNHead)
    class BoundaryCondition(PINNHead)
  Implement Burgers and if time allows Navier Stokes

## Slide 78: Few classes in SciANN
Problem: Equilibrium and BCs are evaluated at ALL collocation points (BC loss is defined in terms of masks). This is simple to implement but inefficient as .

## Slide 79: Few classes in Modulus/SimNet

## Slide 80: Collocation point densification
Before
vedo
  Supports only a few mesh types (PolyData)
No annotations
  Can’t read annotations from files
Point cloud densification
  Points out of bounds
  Points randomly created within a predefined radius
Now
PyVista
  Supports several mesh types
  Compatible with vedo
Annotations
  Reads annotations from files
  Preserve annotations during mesh refinement
Mesh subdivision
  All points inside geometry
  Points created alongside mesh edges

## Slide 81: Collocation point densification (2D)
Points: 5354
Points: 8262
Points: 42558
Execution time: 22.7s (8 CPUs)
Execution time: 13.0s (8 CPUs)
Original
Densified – max edge length: 0.05
Densified – max edge length: 0.02

## Slide 82: Collocation point densification (3D)
Points: 2354
Original
Points: 461122
Execution time: 85.4s (8 CPUs)
Densified - Default

## Slide 83: Distributed training (single-machine multi-GPU)
DataPartitioner
GPU 1
Optimizer
HOST
All-reduce
PINN
Scatter data
GPU 2
Optimizer
PINN
GPU 3
Optimizer
PINN
GPU N
Optimizer
PINN
GPU 1
Optimizer
PINN
GPU 2
Optimizer
PINN
GPU 3
Optimizer
PINN
GPU N
Optimizer
PINN

## Slide 84: Use case: Burgers’ equation
Burger’s equation:
subjected to:
where
https://github.com/sciann/sciann-applications/blob/master/SciANN-BurgersEquation/SciANN-BurgersEquation.ipynb
Solution with SciANN (TensorFlow)
5000 Epochs, Google Colab (GPU), 2 hours

## Slide 85: Implementing distributed training
Colocation points
Equation: 10000 (grid)
BC:
  Upper/Lower: 1000
  Initial: 2000
DataPartitioner
Partitions
Slice of Eq.set
Slice of BC.set
Distributed process
Partition 0
Slice of Eq. set
Slice of BC set
Partition N
Slice of Eq. set
Slice of BC set
for epoch in range(TOTAL_EPOCHS):
training loop
for minibatch in Eq.set:
rank 0
rank N
Forward pass <Eq.Set minibatch>
Forward pass <entire Slice of BC.Set>
Loss = Loss_Eq + Loss_BC
loss.backward()
average_gradients()
(…)
For N=10 parallel process:
Eq.set = 1000 pts
BC.set = 400 pts
average_gradients()
.step()
Optimizer
.step()
Optimizer
All-reduce
training loop
Model
NN graph

## Slide 86: Implementing distributed training
5000 Epochs, 10 process, local CPU (~ 13 min)

## Slide 87: Next use case: 2D laminar flow (steady state)
Coarse mesh
Fine mesh
Inlet velocity profile
Umax = 0.5 m/s
Re = 992
Umax = 1 m/s
Re = 1985
1e-6
1e-6
0.533
1.09

## Slide 88: File system and configuration setup (draft)
./project_name
  /cad
    my_doe.json
    my_cad_01.brep
    my_cad_01.msh
    my_cad_02.brep
    my_cad_02.msh
    …
  /data_trng
    userLib.py
    data_01.vtk
    data_02.vtk
    …
  /pinn
    config.trng
    config.pred
    model.pt (trained model)
    …
  /predictions
    run_01.vtk
    run_02.vtk
    …
my_doe.json
userLib.py
class Inlet(PDE):
  def __init__(self, ...):
  ...
  def forward(self, ...):
Augusto (10 points):
fixed geometry (only Umax),
Parametrized geometry
Andre:
Export densified (collocation) *.vtk (shaft, airfoil, airfoil doe)

## Slide 89: From geometry to visualization of results
Training vs prediction as well as solver configurations can be defined through a file system
AWS-UCF-PINN:
Use FreeCAD
Alternatives:
Fusion360, Inventor, SolidEdge, etc.
AWS-UCF-PINN:
We will design a metafile system (similar to scripts used by other computational mechanics packages).
This is where libraries such as Vedo will be used
1) Geometry
2) Mesh
3) Governing equations
4) Material formulation
5) Boundary conditions
6) Solver
7) Post-processing
PDEs:
Fluid dynamics
Heat transfer
Elasticity
Material properties
Constants
Varying properties
Temperatures, pressures, forces, displacements, etc.
Find solution of PDEs at domain of interest
is usually defined here
3D modeling (primitives, transformations, parametrization, etc.)
Mesh geometrical model or import it from a different application.
Train PINN model
Pick NN architecture
Define loss function
Run optimizer
Predictions with trained PINN model
Dirichlet:
Neuman:
Robin:
Others
Sample domain (space)
Model for
“PINN jargon”
Computational mechanics
Third party
Potential interface with other packages
Bulk of parallelization
AWS-UCF-PINN: Generate results compatible with ParaView
Alternatives:
Most FEA or CFD packages offer it
Our project
AWS-UCF-PINN:
FreeCAD / GMesh
Alternatives:
Most FEA or CFD packages offer it

## Slide 90: PINN 101
Computational mechanics
Finite element modeling
Computational fluid dynamics
Physics-informed neural networks

## Slide 91: Reading
PyTorch stuff
https://github.com/pytorch/pytorch/tree/master/torch
https://pytorch.org/tutorials/beginner/dist_overview.html
https://pytorch.org/tutorials/intermediate/dist_tuto.html
https://pytorch.org/tutorials/intermediate/ddp_tutorial.html
https://pytorch.org/docs/stable/generated/torch.nn.parallel.DistributedDataParallel.html
General stuff
https://hydra.cc/
https://github.com/qd-cae/awesome-CAE
https://www.freecadweb.org/features.php

## Slide 92: File system and configuration setup (draft)
./project_name
  /cad
    inlet.csv
    my_cad_01.brep
    my_cad_01.msh
    my_cad_02.brep
    my_cad_02.msh
    …
  /data_trng
    userLib.py
    data_01.vtk
    data_02.vtk
    …
  /pinn
    config.trng
    config.pred
    model.pt (trained model)
    …
  /predictions
    run_01.vtk
    run_02.vtk
    …
Observations:
data_*.vtk:
  Collocation points, equilibrium, and boundary conditions
  Always needed and should be obtained through a code that reads the originally annotated brep and msh files. This code can eventually do sanity checks regarding the physics.
  Saving vtk files allow users to perform cross-checks before dispatching time-consuming training/predictions.
  Tag using engineering jargon (inlet, no slip, etc.) as opposed to math jargon (Dirichlet, Neuman, etc.)?
config.trng: configuration file for a “training job”
  Neural network architecture / Optimizer setup / Loss function details / Data generator setup (splitting/batching of collocation points) / Execution setup (1. single-device / 2. single-machine multi-GPU)
  A “super-user” could bypass by using our API directly (somewhat similarly to packages such Modulus).
config.pred: configuration file for a “prediction job”
  File with trained model (model.pt) / Data generator setup (splitting/batching of collocation points) / Execution setup
  Set of data_*.vtk files

## Slide 93: Single-machine multi-GPU
DataPartitioner
GPU 1
Optimizer
HOST
All-reduce
PINN
Scatter data
GPU 2
Optimizer
PINN
GPU 3
Optimizer
PINN
GPU N
Optimizer
PINN
GPU 1
Optimizer
PINN
GPU 2
Optimizer
PINN
GPU 3
Optimizer
PINN
GPU N
Optimizer
PINN

## Slide 94: Single-machine (cluster) multi-GPU
DataPartitioner
GPU 1
GPU 2
GPU 3
GPU N
Optimizer
HOST
Broadcast
Gather/
Reduce
PINN
PINN
PINN
PINN
Scatter data
DOE points:

## Slide 95: Parallel/distributed training
https://pytorch.org/blog/introducing-pytorch-fully-sharded-data-parallel-api
https://pytorch.org/xla/release/1.11/index.html
https://pytorch.org/tutorials/beginner/dist_overview.html
https://pytorch.org/tutorials/intermediate/dist_tuto.html

## Slide 96: Snippets of code: Burgers’ equation
def run(epochs=10, verbose=False):
accelerator = Accelerator()
...
train_dataloader = torch.utils.data.DataLoader(train_set, batch_size=bsz, shuffle=True)
train_bc_dataloader = torch.utils.data.DataLoader(train_set_bc, batch_size=bsz_bc, shuffle=True)
model = Net()
model = model
optimizer = optim.Adam(model.parameters(), lr=0.002)
model, optimizer, train_dataloader, train_bc_dataloader = accelerator.prepare(
model, optimizer, train_dataloader, train_bc_dataloader
)
...
for epoch in tqdm(range(epochs), disable=not accelerator.is_local_main_process):
...
for data in train_dataloader:
...
loss_eq = F.mse_loss(f, torch.zeros_like(f))*torch.tensor(1)
loss_bc = F.mse_loss(model(bc_data), bc_target)*torch.tensor(1)
# warm-up only with eq
if epoch<5:
loss = loss_eq
else:
loss = loss_eq + loss_bc
...
accelerator.backward(loss)
optimizer.step()
...
if (epoch+1) % 10 == 0:
avg_loss = epoch_loss / num_batches
accelerator.reduce(avg_loss, 'mean')
accelerator.wait_for_everyone()
if accelerator.is_main_process:
if verbose:
print(f'Avg Loss at epoch {epoch}: {avg_loss}')
if avg_loss < best_loss:
if verbose:
print(f'Avg Loss improved from: {best_loss} to {avg_loss}')
best_loss = avg_loss
unwrapped_model = accelerator.unwrap_model(model)
accelerator.save(unwrapped_model.state_dict(), 'burgers_model.pt')
if verbose:
print("Model saved in burgers_model.pt")
Implementation using Accelerate
Accelerate config file for a 2-GPU Linux machine
Config file generated for launching script

## Slide 97: Running on a 2-GPU Linux machine
Same screenshot that Renato has generated, but with Andre’s user account
Live demo?